PROJECT INFORMATION DOCUMENT (PID)

CONCEPT STAGE

Report No.:  AB1757

| Project Name | AMMAN EAST POWER PLANT |
| --- | --- |
| Region | MIDDLE EAST AND NORTH AFRICA |
| Sector | Power (100%) |
| Project ID | P094306 |
| Borrower(s) | JORDAN (GUARANTOR) |
| Implementing Agency |  |
|  | Ministry of Energy & Mineral Resources Jordan |
|  | TBD – private sector special purpose company |
| Environment Category | [X] A [ ] B [ ] C [ ] FI [ ] TBD (to be determined) |
| Date PID Prepared | July 6, 2006 |
| Estimated Date of Appraisal Authorization | October 3, 2006 |
| Estimated Date of Board Approval | March 8, 2007 |

- Key development issues and rationale for Bank involvement

Key Development Issues

To reduce a potential fiscal deficit and address the priority issues of poverty reduction and job creation, the Government of Jordan (GoJ) sees the need to create an environment conducive to private investment, by establishing a good investment regime to strengthen fiscal stability, build up human resources and ensure sustainability.

On energy supply, GoJ moved to lift prices of domestic fuels as the twin pressures of high international oil prices and the ending of the Saudi Arabian oil supply agreement in April 2005 became fiscally unbearable and a major contributor to the fiscal deficit.  Furthermore, as part of a decade-long structural reform of its economy, Jordan has sought to diversify the fuel mix and supply sources in order to reduce dependence on imports and use of oil, the consequent adverse balance of payments situation and negative environmental impacts.  Increasing the share of natural gas significantly, promoting renewable energy sources (wind, solar, biogas and geothermal), and promoting energy use efficiency are the three principal means through which the Government of Jordan seeks to achieve a more sustainable energy balance in the future.

The Government has been actively looking at ways to promote exploration and development of energy resources in Jordan, particularly oil, gas, and oil shale.  It has adopted a new Electricity Law and the unbundling of the power sector has been completed.  The regulatory authority for the power sector, the Electricity Regulatory Commission (ERC) has been set up.  A good start has been made with the gradual price increase of petroleum product prices to bring them in line with international market prices. The power sector is financially viable. It does not receive explicit financial subsidies from the Government budget, but it has benefited from the use of natural gas from Egypt at relatively favorable prices and some subsidies on petroleum products.  The structure of retail tariffs has still some element cross subsidies and could be improved. ERC has initiated a tariff review.  Most of the distribution sector is already owned by the private sector and the Government plans to further divest its shares in EDCO and IDECO.  It is expected that the privatization of Central Electricity Generating Company (CEGCO), the generation company, will be successfully completed in the months to come.  The Government is also considering privatizing the SAMRA generation company through an IPO.  The proposed project would be the first fully privately owned power generation station.  The Government has sought the assistance of the Global Environment Facility (GEF) to reduce barriers to adopting renewable energy, and GRF has responded favorably to the preparation of a wind project of about 60MW.  The Government has also requested assistance for establishing an energy efficiency fund.

Jordan began importing natural gas from Egypt in 2003 and most of its generation plant is now operating on this fuel.  Future thermal generation, including the current project, will predominantly use natural gas, and will be complemented by renewable sources such as wind.

The current peak demand for electricity on the interconnected system in Jordan is about 1,500MW.  The installed capacity today is about 1,800MW, a reserve margin of about 20%.  However, the growth rate in electricity consumption is forecasted to be about 3.5% per annum (mid-case), which indicates that the reserve margin will evaporate by 2010- which is very soon in investment planning and implementation terms.  Therefore, to maintain a prudent reserve margin, the Government has initiated work on the proposed project, which is intended to bring additional capacity of 280-450MW in 2007-2008.

Rationale for Bank Group Involvement

Partial Risk Guarantees (PRGs) and MIGA insurance are suited to helping governments transition from public to private finance through political risk mitigation and effective risk sharing with project sponsors and lenders.  The Request for Proposals for the proposed project therefore included a joint Bank Group statement of in-principle support for the project.  This, as well as the transparent bidding process that satisfied the Bank’s requirement for economy and efficiency, have helped the Government attract competitive proposals for the project.

Several private sector projects have failed to materialize in Jordan.  In the power sector, Samra did not proceed as a private sector project, in part because of uncertainty on the source of fuel for the power plant, and the fact that the selected private promoter withdrew its support for reasons unrelated to the project.  The Disi Amman water supply project also failed, because the bid tariff was much higher than anticipated.  Such lessons are being applied to this project by, for instance, ensuring that the fuel supply arrangements and a minimum regulatory framework to give comfort to the bidders were in place prior to bid issuance.  Also, ensuring there is commitment to the project in Jordan and all stakeholders are on the same page.  A challenge for both the Bank and the Government is to ensure that this project is a catalyst for wider PSP in infrastructure.

- Proposed objective(s)

The main objective of the project is to meet the electricity needs of the country in an economically and environmentally sustainable manner to contribute to economic growth and well-being of the population of Jordan.  The project would add about 370 MW of additional power to the system, help to ensure the reliability of power supply and help maintain a margin between available capacity and demand of at least 10%.  The purpose of the PRG is to enhance competition and therefore help reduce the project’s financing costs.

- Preliminary description

The proposed project consists of a 370 MW gas-fired combined-cycle power station to be developed, owned, and operated by a private-sector project company.  The US$310 million power station will be constructed on a site located at Almanakher, east of Amman Jordan and about 1 km from the Jordanian Gas Transmission Pipeline.  The fuel supply will be natural gas from Egypt; Heavy Fuel Oil (HFO) will serve as backup fuel for emergency operations only.  The first phase of the power station will comprise two simple-cycle gas turbines.  The second phase will add a Heat Recovery Steam Generator and thus increase the capacity by 50%.  The water for steam generation will be provided by the Water Authority of Jordan.

The proposed contractual structure of the transaction is consistent with industry standards with respect to the allocation of commercial, technical, and political risks among the parties in a limited recourse project financing structure.

Public sector involvement in the project

The contractual structure includes the following principal agreements with the Government, or state-owned or state-controlled entities, all of which will be coterminous with the Implementation Agreement:

- Implementation Agreement

- Government Guarantee

- Power Purchase Agreement

- Fuel Supply Agreement (may be tolling agreement)

- Water Supply Agreement

- Land Lease Agreement.

Private sector contracts

The Government will not be a party to the following major contractual arrangements:

- Engineering, Procurement, and Construction Contract (EPC Contract)

- Operations and Maintenance (O&M) Contract

- Financing agreements

- Insurance.

- Safeguard policies that might apply

The project involves construction and operation of a new power station and is Category A.  The power station site is owned by the Government of Jordan.  The Government is in process of collecting baseline environmental data.  In compliance with OP 4.01, the successful bidder will be required to engage independent experts to conduct an Environmental Assessment (EA), including public consultations.  The EA will reveal the other safeguards policies that apply to the project, if any.

The successful bidder will be required to prepare and implement an Environmental Management Plan (EMP) for the project.

- Tentative financing

| Source: | ($m.) |
| --- | --- |
| BORROWER | 10 |
| FOREIGN PRIVATE COMMERCIAL SOURCES | 300 |
| IBRD GUARANTEE | 00 |
| Total project cost | 310 |

- Contact point

Contact	 Reynold Duncan

Title	 Sr Power Engineer

Tel	 (202) 458-4609

Fax	 (202) 477-1998

Email	 Rduncan1@worldbank.org