PROCUREMENT PLAN FOR ARICO SUB-PROJECT PROPOSAL

#### Imported package

| Code | Number of package | Description | Estimate Cost (USD) | Procurement Method | Expected bid/proposal invitation Date | Expected Contract Award Date | Contract Implemen tation Period | Review by the PMU | Review by the Bank |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | Cyclo-pentane storage system | As specified in the PIM of the HCFC phase out Project | Q1 - 2014 | Q1 - 2014 | Q1-3/2014 | Prior | Post |
|  |  | 01 set of 500 lt Cyclo-pentane storage tank & pneumatic C5 loading pumps Piping and accessories from C5 drums to tank. 01 lot of rigid piping from C5 storage to Premix unit |  |  |  |  |  |  |  |
|  |  | Cyclo-pentane Pre-mixing and blending Station |  |  |  |  |  |  |
|  |  | 01 set of Pentane Premix Unit completed with Polyol circuit, Metering and Control panel, including rigid piping to buffer tank. |  |  |  |  |  |  |  |
|  |  | 01 set of 1,000lt Raw Polyol storage tank including transfer unit, completed with chiller, other auxiliaries, and piping to Premix. |  |  |  |  |  |  |  |
|  |  | 01 set of 1,000lt blended Polyol+ pentane buffer tank including piping to foaming machines, transfer unit, completed with magnetic coupling, chiller and other auxiliaries. |  |  |  |  |  |  |  |
|  |  | Foaming lines |  |  |  |  |  |  |
|  |  | High pressure Polyol pentane modules (Max output 200kg/min x 2) for conversion of Polyol modules of 02 existing Cannon foaming machines, completed with full auxiliaries 01 lot of High pressure rigid piping and flexible hose Nitrogen purging valves for two mix heads |  |  |  |  |  |  |  |
|  |  | Ventilation Fans |  |  |  |  |  |  |
|  |  | 01 lot of Spark-free ventilation fans for the following areas: 02 Spark Free 8,000 m3/h Centrifugal Fan with 3Ø AC motor for Pentane storage and Premix 01 no. Spark Free 15,000m³/h and 02 spark free 4,000m3/h with 3Ø AC motor for Panel foaming line |  |  |  |  |  |  |  |
|  |  | Safety systems for gas handling |  |  |  |  |  |  |
|  |  | 02 sets of Electrical control Safety Panel for the following areas: Pentane storage and Premix Panel foaming line with 2 retrofitting foaming machines |  |  |  |  |  |  |  |
|  |  | 01 lot of 16 Hydrocarbon sensors/detectors |  |  |  |  |  |  |  |
|  |  | 01 set of Remote equipment for Alarm System |  |  |  |  |  |  |  |
|  |  | Installation & Commissioning of equipment inclusive of training, preliminary discussion, project kick off site visits and post-conversion visit. Sea freight, Packing and Fumigation. |  |  |  |  |  |  |  |
|  |  | Sub-Total |  |  |  |  |  |  |  |

#### Local purchasing packages

| Code | Number of package | Description | Estimate cost (USD) | Procurement Method | Expected bid/proposal invitation Date | Expected Contract Award Date | Contract Implementation Period | Review by the PMU | Review by the Bank |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Dry plant retrofitting | As specified in the PIM of the HCFC phase out Project | Q2 – 2014 | Q2 – 2014 | Q2-3/ 2014 | Prior | Post |
| 1 | 1 | Retrofitting of 03 existing discontinuous presses to be ready for Pentane usage |  |  |  |  |  |  |  |
| Ducting System |  |  |  |  |  |  |
| 2 | 1 | Ducting system for Panel foaming lines and premix room |  |  |  |  |  |  |  |
| Safety systems for gas handling: |  |  |  |  |  |  |
| 3 | 1 | Back-up power system (EPS) – Stand by Generator to run the ventilation fans and safety panel, including ATS, wires and cables. |  |  |  |  |  |  |  |
|  |  | Nitrogen Generator System |  |  |  |  |  |  |  |
| 4 | 1 | Water Sprinkler |  |  |  |  |  |  |  |
|  |  | Fire hose reel |  |  |  |  |  |  |  |
|  |  | Portable fire extinguishers |  |  |  |  |  |  |  |
| 5 | 1 | Anti static floor covering |  |  |  |  |  |  |  |
| 6 | 1 | Safety audit and Certification | Fully borne by Arico Co., Ltd |  |  |  | Under PMU supervision to ensure availability of safety audit before production start-up | Post |
| 7 | 1 | Trials for validation of formulations: purchasing of chemicals and other utilities |  | Direct Contract | Q3 – 2014 | Q3 – 2014 | Q3 - 2014 | Prior | Post |
|  |  | Sub-total |  |  |  |  |  |  |  |
|  |  | IOC claim (US$ 90,400 of IOC will be used for ICC) |  |  |  |  |  |  |  |
|  |  | Grand Total (including part A + B + IOC Claim) |  |  |  |  |  |  |  |

- Note:

Partial IOC will be used for ICC and ARICO Co., Ltd will pay the amount that exceeds the sub-grant ceiling. In case the bidding price is lower than sub-grant ceiling, the PMU will pay the bidding price.